## Slide 1: Computer Organization

## Slide 2: Computer System
Hardware
Software

## Slide 3: Computer Hardware
A typical computer system consists of the following major components:
The central processing unit (CPU)
Main memory
Secondary storage devices
Input devices
Output devices

## Slide 4: Computer Hardware

## Slide 5: The organization of the CPU
Arithmetic & Logic unit (ALU)
Control
unit
COORDINATES ALL OF THE COMPUTER’S OPERATIONS
ALU is designed to perform mathematical operations

## Slide 6: CPU images

## Slide 7: THE CPU’S JOB

## Slide 8: THE CPU’S JOB
Fetch:
The CPU’s control unit fetches, from main memory, the next instruction in the sequence of program instructions
CPU
RAM

## Slide 9: THE CPU’S JOB
Decode:
The instruction in encoded in the form of a number. The control unit decodes the instruction and generates an electronic signal

## Slide 10: The job CPU
Execute:
The signal is routed to the appropriate component of the computer (such as the ALU, a disk drive, or some other device). The signal causes the component to perform an operation
CPU
RAM
DISK DRIVE

## Slide 11: Computer internal memory
RAM (Random Access memory)
ROM (Read only memory)
Cache memory

## Slide 12: RAM

## Slide 13: RAM
RAM (Random Access Memory) is a device that holds information
RAM holds the sequence of instructions in the programs that are running and the data those programs are using

## Slide 14: RAM
Main memory is an ordered sequence of cells, called memory cells
Each cell has a unique location in main memory, called the address of the cell
When the computer is turned off, RAM loses its data

## Slide 15: Memory capacity
Prefix | Symbol | Exponential | Numeric | Binary | Decimal value
Kilo | K | 10^3 | 1,000 | 2^10 | 1024
Mega | M | 10^6 | 1,000,000 | 2^20 | 1,048,576
Giga | G | 10^9 | 1,000,000,000 | 2^30 | 1,073,741,824
Tera | T | 10^12 | 1,000,000,000,000 | 2^40 | 1,099,511,627,776
Peta | P | 10^15 | 1,000,000,000,000,000 | 2^50 | 
Exa | E | 10^18 | 1,000,000,000,000,000,000 | 2^60 | 
Zatta | Z | 10^21 | 1,000,000,000,000,000,000,000 | 2^70 | 
Yotta | Y | 10^24 | 1,000,000,000,000,000,000,000,000 | 2^80 | 

## Slide 16: Binary Number System
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
2^7 | 2^6 | 2^5 | 2^4 | 2^3 | 2^2 | 2^1 | 2^0
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
Byte

## Slide 17: Bit VS Byte
Bits are used to measure data transfer speed rate as Internet connection (Example: 25Mbps)
Bytes are used to measure file size and storage capacity (Example: 2GB)

## Slide 18: DDR2 VS DDR3 VS DDR4 RAM
Feature | DDR2 | DDR3 | DDR4
TRANSFER RATE | 400 MB/S – 1066 MB/S | 800MB/S-2133MB/S | 1600MB/S-3200MB/S
MEMORY DENSITY |  | 512MB – 8GB | 2GB – 16GB
VOLTAGE | 1.8 VOLTS | 1.5 BOLTS | 

## Slide 19: Secondary storage devices
Hard disk drive (HDD) (External & Internal)
  Magnetic HDD
  Solid State Drive (SSD)
  Hybrid HDD
DVD
Blu Ray
Flash Memory

## Slide 20: Magnetic HDD VS SSD
HDD VS SSD

## Slide 21: USB PORTS

## Slide 22: HDMI PORT

## Slide 23: CELLULAR NETWORT
Type | Speed Rate
3G | 144 Kbps - 400 Kbps
4G | 5 Mbps - 12 Mbps

## Slide 24: Character representations in memory
Character | ASCII (IN DECIMAL) | UNICODE (IN DECIMAL) | BINARY CODE
# | 35 | 35 | 00100011
$ | 36 | 36 | 00100100
0 | 48 | 48 | 00110000
1 | 49 | 49 | 00110001
A | 65 | 65 | 01000001
B | 66 | 66 | 01000010
a | 97 | 97 | 01100001
b | 98 | 98 | 01100010

## Slide 25: SATA Explanation - Ports, Cables, Controllers, Motherboards
SATA and IDE cables

## Slide 26: Numbering systems
Decimal (0 … 9)10
Binary (0 … 1)2
Hexadecimal (0 … 9, A, B, C, D, E, F)16
(0 … 9,10,11,12,13,14,15)16
Octal (0 … 7)8

## Slide 27: Hexadecimal Number System
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
8 | 4 | 2 | 1 | 8 | 4 | 2 | 1
2^3 | 2^2 | 2^1 | 2^0 | 2^3 | 2^2 | 2^1 | 2^0
3 |  |  |  | 3 |  |  | 
Byte | 
First digit | Second digit

## Slide 28: Octal Number System
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
2 | 1 | 4 | 2 | 1 | 4 | 2 | 1
2^1 | 2^0 | 2^2 | 2^1 | 2^0 | 2^2 | 2^1 | 2^0
2 |  | 5 |  |  | 6 |  | 
1 | 0 | 1 | 0 | 1 | 1 | 1 | 0
Byte |  | 
First digit | Second digit | Third digit
2 Bit | 3 Bit | 3 Bit

## Slide 29: Computer Software
Operating System software
Application software

## Slide 30: Operating System software
Windows
OS X operating system (MAC computers)
Linux
UNIX

## Slide 31: Operating System software difference
Security
Stable
User friendly
Ease of use
Multimedia capabilities